## Slide 1
Air pollution, risk and vulnerability to heat in the city of Abidjan (Côte d'Ivoire) :
Preliminary results
Conclusion/Implications
Methods
Results
References
Air pollution in African cities causes a significant burden of respiratory diseases, exacerbated by increased heat intensity in Abidjan. In some districts in Abidjan, low-income households have limited choices of combustion energy (wood, charcoal), making them vulnerable to indoor air pollution. This exposure to heat and air pollution simultaneously can increase the risk of mortality related to respiratory diseases (Areal, 2022).
This study aimed to understand the synergistic effects of heat and air pollution on people's health in Abidjan.
These preliminary results show that PM2.5 concentrations in Abidjan are very high and above WHO standards.
This high levels of PM2.5 pollution requires to develop mitigation strategies and concrete recommendations aimed at reducing pollution in Abidjan.
It will be important to understand the link between air pollution, high temperatures and the impact on the health of populations in Abidjan.
The modeling work is in progress.
Figure 1: Relationship between Indoor vs Outdoor PM2.5 and Temperature
- Both indoor and outdoor levels exceeded WHO standards
- Indoor concentrations were consistently higher than outdoor levels
-This higher indoor exposure particularly affects vulnerable groups who spend more time at home (children and elderly)
Figure 2 : Boxplot data from PM2.5 Indoor and outdoor in Vridi
-indoor box (orange) is higher, with a median around 60 µg/m³ compared to ~45 µg/m³ outdoors.
-Indoor data also shows greater variability, indicating more frequent and intense pollution peaks.
-Even extreme outdoor values do not reverse this trend
- WHO recommended threshold (15 μg/m³) is indicated by a red dashed line
- Measured PM2.5 indoor concentrations ranged from 15.15 to 165.75 μg/m³
Areal, A.T.; Zhao, Q.; Wigmann, C.; Schneider, A.; Schikowski, T. The Effect of Air Pollution When Modified by Temperature on Respiratory Health Outcomes: A Systematic Review and Meta-Analysis. Science of the Total Environment 2022, 811, 152336
Carvalho, H. New WHO Global Air Quality Guidelines: More Pressure on Nations to Reduce Air Pollution Levels. The Lancet Planetary Health 2021, 5, e760–e761.
Authors: Madina DOUMBIA1,2* ; Etienne KOUAKOU2,3 ; Iba Dieudonne DELY1,2 ; Véronique YOBOUE4 ; Matthew CHERSICH5 ; Stanley LUCHTERS6; Brama KONE1,2 ; Guéladio CISSE1,2,7,8, on behalf of the HE 2AT Center
1.University Peleforo Gon Coulibaly, Côte d’Ivoire ; 2.Centre Suisse de Recherches Scientifiques en Côte d’Ivoire ; 3 University Nangui Abrogoua, Côte d’Ivoire ; 4 University Felix Houphouët Boigny, Abidjan, Côte d’Ivoire; 5. Witwatersrand University, Johannesburg, South Africa ; 6.Center for Sexual Health and HIV/AIDS Research, Harare, Zimbabwe ; 7.Swiss Tropical and Public Health Institute, Allschwil, Switzerland ; 8.University of Basel, Basel, Switzerland ; *.Presenting author
Air pollution measurements using low-cost sensors PurpleAir, October 2024 to now), provide real-time data on Particulate Matter (PM) in three settlement areas in Abidjan (Vridi, Williamsville and Yopougon).
Background
Box-plot was used to understand the distribution of PM2.5 observations and identify extreme values. Temperature for the same periods (data from sensors) with air pollution data are then used to understand relationships between the 2 variables.
Figure 1
Figure 2
Table1
Results
Table 1:PM2.5 analysis - Abidjan (Vridi, Williamsville and Yopougon, October 2024 to now)
-Indoor temperatures were consistently higher than outdoors
All PM2.5 average levels far exceed WHO standards (15 μg/m³)
-High variability indicates unstable and dangerous pollution levels.
-Indoor pollution exceeds outdoor in Yopougon and Vridi ➜ likely due to poor ventilation and internal sources.
-Serious health risk in William, especially outdoors ➜ urgent need to investigate pollution sources.
Funding National Institutes of Health (NIH) / Fund for Science, Technology and Innovation (FONSTI) ; Contact : doumbiamadina@upgc.edu.ci